## Slide 1: DESIGN VALIDATION PRESENTATION
USASOC 36 Quiet Drone

## Slide 2: UPDATES FROM FDP

## Slide 3: MS PROJECT UPDATES

## Slide 4: Gantt Chart

## Slide 5: MS PROJECT BUDGET UPDATE
REMAIN BUDGET | 732.85
Bought already | price(USD)
Holy Stone HS120D | 200.8
noise decibel meter | 50
Stereo Enclosed speaker | 7.5
mini usb microphone | 5.95
mini oval speaker | 1.95
wired mini electric mic | 0.95
rasberry pi zero | 0
Things to update MS Budget with:​
Power Supply​
More Speakers​
Prop Materials​
Rasberry Pi zero
Click to add text
2%

## Slide 6: RESOURCE, SKILLS, TOOLS, & PARTS INVENTORY
Altium Design, Fusion 360, Oscilloscope, Soldering Iron, Raspberry Pi Zero, 18650 4 Ah 3.7 V Li-on Battery, PCB Voltage Regulator.
Learned/improved skills since FDP:
  Nasa: LabVIEW
  Chris: Fusion 360
  Minh: Altium Design, Fusion 360
  Mayra: MATLAB coding
  Yewen: MATLAB coding, soldering & grinding
  Ivette: Python Coding
  Maryam: Raspberry Pi coding

## Slide 7: WEEKLY MEETING SCHEDULES, & ROLE UPDATES
The virtual meeting with technical mentor is set every Tuesday 9am to 10am.
The group in-person meeting is set every Wednesday at 4pm to 5pm.
Nasa Tafari: PCB and Hardware Design of active noise cancelling system
Minh Nguyen: PCB and Hardware Design of active noise cancelling system
Yewen Huang: Assembling, implementing and testing devices
Mayra Teixeira: MATLAB Software for analyzing noise data
Chris Fleurima: Fusion 360 Software for designing ANC casing and drone propellers.

## Slide 8: 5 PROJECT-SPECIFIC SUCCESS CRITERIA (PSSC)
1. Functions of ANC system can be proved by stationary simulation.
2. The ANC system is reliable and works in practicality.
3. The noise reduction is achieved by the improvement of hardware design through propellor design.
4. The assurance of duration of flight.
5. The maneuverability is not compromised.

## Slide 9: DESIGN VERIFICATION & VALIDATION PLAN
3. Redesign hardware (Ex. Propellers, shrouds) to attain 5dBA of noise decrease when the drone is in pre-flighting mode at 4 feet below, 4 feet away from the decibel measuring devices.
4. Testifying the duration of flight of drone should be over 10 minutes at hovering with onboard ANC system.
5. Ensuring maneuverability of the drone should not be generally easily controllable; every member in our team should be able to successfully hover the drone in a designated area without difficulty.
1. Introduce MATLAB plots and data to demonstrate theoretical ANC system capabilities with a factor of safety (10dBA)
2. Testifying onboard ANC system in those scenarios:
(1). At least decreasing 3dBA while the drone is in pre-flighting mode at 4 feet below, 4 feet away from the decibel measuring devices,
(2). At least decreasing 5dBA in hovering while the drone is flighting at 2 feet above, 4 feet away from the decibel measuring devices,
(3). At least decreasing 5dBA in full load speed at least decreasing 7dBA in hovering while the drone is flighting at 6 feet above, 4 feet away from the decibel measuring devices,

## Slide 10: DESIGN VALIDATION
Design Validation: describe your verification tests (at least 5), why they help assessing how your project is responding to the initial customer requirements and problem definition. Please list the original requirements and any agreed on modifications, and explain how each test will help with the performance measurement, electrical safety, ethics of fairness to all parties involve, etc

## Slide 11: VALIDATION DATA
results from your verification validation tests, sources of validation data and comparisons. Use of ML through randomization of training and validation data to perform polynomial regression on your data to obtain the best model, and/or show how your trained your algorithm to recognize a particular pattern. This requires data measurements rather than P/F validation tests. (20%)

## Slide 12: 3-D PCB Design For Regulator

## Slide 13: 2-D PCB Design For Regulator

## Slide 14: PCB: reasoning, functionality, and performance (simulation and validation data)

## Slide 15: CAD CASING FOR ANC

## Slide 16: PRELIMINARY DATA SETUP

## Slide 17: PRELIMINARY DATA
Team 3 tested the three scenarios: hovering without modification, pre-flight without modification and full-flight. The data presented here is for hovering without modification.
Explanation: A Fourier Transform and A-weighting filter were applied to the the signal of hover without modification.
Currently we are writing a code to apply a filter to the original signal to remove the three target frequencies and then invert the signal(applying Fast inverse Fourier Transform). The goal is to find the noise reduction theoretically.

## Slide 18: INITIAL LabVIEW SIMILUATION

## Slide 19: Computer grahics and at least one short video of the system

## Slide 20: PROJECT DELIVERABLES
ANC system program.
A working model for the ANC system .
3D printed case for ANC.
3D printed propellers.
Data from experiments and research for archives.
A system capable of reducing the noise of a drone by 5dBA
Notes: A system with ANC that would reduce the noise by…..

## Slide 21
Anticipated problem and solution for the final product; Deliverables: confirmation and/or adjustment (Preview of the Final Product Presentation) (5%

## Slide 22: TEAM SAS SURVEY
How would you rate our overall communication, organization, and participation?
Average Rating = 4.43
Rate your contributions of work that has been done for the project and each other team members?
Average personal score = 4.3
Rate the contributions for each other team members?
Average team rating = 4.42
Has the team lead and co-met your expectations for a lead?
Average rating = 4.495

## Slide 23: TEAM SAS SURVEY
How would you rate your teams project design, in terms of design constraints, engineering requirements, feasibility, and difficulty?
Average rating = 4.52
How would you rate the support the team has from the university?
Average rating = 3.71
How confident are you that the team will continue to meet goals/deadlines?
Average rating = 4.57
Will the final design product meet all the requirements giving the current outcomes?
Average rating = 4.43

## Slide 24: APPROVALS
DocuSign approval from all team members, CM, TM

## Slide 25: Questions?